## Slide 1
CLOUD INFRASTRUCTURE
Cloud File Backup
& TCP Behaviour
Why bulk data transfer over TCP is harder
than it looks — and how to get it right
Dimitrios Dalaklidis | Computer Networks | University of Western Macedonia

## Slide 2
What Cloud Backup Actually Needs from TCP
Cloud backup is not like web browsing. It has a distinct performance profile that shapes every TCP design decision.
HIGH PRIORITY
Reliability
Every byte must arrive intact. Data loss in a backup is unacceptable — TCP's ACK and retransmission mechanisms are non-negotiable here.
HIGH PRIORITY
Throughput
Large volumes of data must transfer efficiently. Congestion control must not throttle bandwidth more than necessary on stable links.
LOW PRIORITY
Latency
Backup jobs run in the background. A few extra milliseconds of RTT are irrelevant — unlike real-time video or interactive apps.
ACTIVE RISK
Fairness
Aggressive backup flows can crowd out other traffic on shared links. TCP must self-regulate to avoid degrading the wider network.

## Slide 3
Where TCP Struggles in Cloud Backup Environments
Three structural challenges that degrade backup performance — even when the network looks healthy.
01
RTT Variability & Timeout Sensitivity
Cloud datacenters introduce geographic distance, multi-tenant shared infrastructure, and dynamic routing — all of which cause RTT to fluctuate unpredictably.
A poorly calibrated RTO triggers unnecessary retransmissions (too small) or delays loss detection (too large). Both outcomes increase total transfer time.
Root cause: RTO miscalibration
02
Bufferbloat from Aggressive Window Growth
Loss-based algorithms like CUBIC grow the congestion window aggressively until a packet is dropped. In cloud environments with large buffers, this fills queues before loss is detected.
The result: high throughput on paper, but inflated RTT and degraded responsiveness for all other traffic on the link.
Root cause: Buffer overfill
03
Fairness Under Concurrent Flows
Backup jobs are long-lived, high-volume flows. Running alongside interactive traffic (web, video calls), they can starve other connections — especially when TCP congestion control does not self-limit.
AIMD helps, but the balance between backup speed and network fairness requires deliberate tuning.
Root cause: Flow dominance
Key insight: These are not failures of TCP — they are design trade-offs that become visible at cloud scale.

## Slide 4
What Actually Works: Mechanisms & Recommendations
MECHANISMS THAT HELP
SACK (Selective Acknowledgment)
Allows the receiver to acknowledge non-contiguous data blocks, so the sender only retransmits exactly what was lost — not everything after the gap. Critical for high-latency cloud links.
RTT Smoothing
Weighted averaging of RTT samples (as per RFC 793) produces a stable RTO estimate, preventing both over-eager retransmissions and delayed loss detection in variable-RTT cloud environments.
Slow Start + AIMD
Gradual window growth prevents buffer flooding on connection setup. Additive increase / multiplicative decrease ensures fair bandwidth sharing with concurrent flows over time.
TCP BBR (for bulk transfers)
Models bottleneck bandwidth and propagation RTT directly, avoiding bufferbloat. Outperforms CUBIC for large backup flows on LTE and similar high-bandwidth variable links.
DECISION GUIDE
Large files, stable link?
BBR
Small files, mixed traffic?
CUBIC
High RTT variance?
Enable SACK + RTT smoothing
Shared network link?
Tune AIMD, monitor fairness
Bufferbloat observed?
Switch to BBR
Source: Li et al., PAM 2017; RFC 793; RFC 2018 (SACK); Le Boudec & Thiran, Network Calculus, 2001